## Slide 1: Binary and hexadecimal numbers

## Slide 2: Outline
In this lesson, we will:
  Learn about the binary numbers (bits) 0 and 1
  See that we can represent numbers in binary
  Quickly introduce binary arithmetic and multiplication
    It is completely parallel to decimal addition and subtraction
  Consider a more compact representation: hexadecimal
    The translation between binary and hexadecimal uses a very simple look-up table

## Slide 3: Counting
We count in base 10 (called decimal counting), meaning we have 10 unique digits, and then we use a positional number system to represent larger numbers
  Once we get to the largest number in any position, we increment the next highest unit
Base 10 is really only useful for humans: we have ten fingers
  Our clock, however, is a hybrid:
    There are 60 seconds in a minute
    There are 60 seconds in an hour
    There are 24 hours in a day
  You know that
    One second after 23:59:59 is 0:00:00 the next day
    The next highest number after 999 is 1000

## Slide 4: Counting
Base 10 is great for humans: we have five fingers on each hand
It’s more difficult for computers:
  Numbers are stored as voltages
    If you want ten different voltages representing ten different digits, you must recognize and store these voltages—this is very difficult
  It is easier to store, access and manipulate just two voltages:
    Say 0 V and 5 V
  This leaves us with two digits only, say 0 and 1
  We will describe 0 and 1 as binary digits or bits

## Slide 5: Counting in binary
If we only accept two bits (0 and 1, or 0 V and 5 V), it may seem much worse, but it’s still manageable:
0b0
0b1
0b10
0b11
0b100
0b101
0b110
0b111
0b1000
0b1001

## Slide 6: Counting in binary
Question: Is 100 equal to 102 or 4?
  We will usually:
    Prefix binary numbers with "0b"
    Use the monospaced typeface Consolas
  Thus:
    100011010 is a large decimal number
    0b11110110010 is binary for 1970
  To start, we will gray-out the "0b"

## Slide 7: Counting in binary
These first ten non-zero binary numbers could therefore represent the number of “I”s shown here
0b0
0b1
0b10
0b11
0b100
0b101
0b110
0b111
0b1000
0b1001
0b1010
0b1011
I
II
III
IIII
IIIII
IIIIII
IIIIIII
IIIIIIII
IIIIIIIII
IIIIIIIIII
IIIIIIIIIII

## Slide 8: Counting in binary
Normally, however, we just indicate the decimal number that it is equivalent to
0b0 0
0b1 1
0b10 2
0b11 3
0b100 4
0b101 5
0b110 6
0b111 7
0b1000 8
0b1001 9
0b1010 10
0b1011 11

## Slide 9: Counting in binary
In decimal, each successive digit represents a higher power of ten:
10 101
100 102
1000 103
10000 104
In binary, each successive digit represents a higher power of two:
0b10 21 = 2
0b100 22 = 4
0b1000 23 = 8
0b10000 24 = 16

## Slide 10: Counting in binary
There are only 10 types of people in the world.
Those who understand binary,
and those who do not.

## Slide 11: Binary integers
For example, in decimal, the number
280973
represents
2 × 105 + 8 × 104 + 0 × 103 + 9 × 102 + 7 × 101 + 3 × 100
In binary, the number
0b101010
represents
1 × 25 + 0 × 24 + 1 × 23 + 0 × 22 + 1 × 21 + 0 × 20 = 42

## Slide 12: Binary real numbers
Similarly,
280.973
represents
2 × 102 + 8 × 101 + 0 × 100 + 9 × 10–1 + 7 × 10–2 + 3 × 10–3
In binary, the number
0b101.010
represents
1 × 22 + 0 × 21 + 1 × 20 + 0 × 2–1 + 1 × 2–2 + 0 × 2–3
4 + 1 + 0.25 = 5.25
Note: Every decimal integer is followed by an implied decimal point
Every binary integer is followed by an implied radix point
Uses a “decimal point”
Uses a “radix point”

## Slide 13: Addition
Just like addition with decimal numbers, you can do the same with binary, you only have to remember:
  1 + 1 = 10 and 1 + 1 + 1 = 11
1 1 1
3725
+ 8982
12707
1 1 1 1 1 1 1 1
9275948135782
+ 503292582385322553
503301858333458335
1 1 1 1
1010
+ 111
10001
1 1 1 1 1 1 1 1 1 1
1110010001100111
+ 110111011011000110
1000101101100101101

## Slide 14: Multiplication
Just like multiplication with decimal numbers, you perform the same operations here, too, only it is easier, just more tedious
359801
× 4327
2518607
7196020
107940300
+ 1439204000
1556858927
42
× 61
42
+ 2520
2562
111011
× 1011
111011
1110110
00000000
+ 111011000
1010001001
1100101110000010
× 101000101
1100101110000010
0000000000000000
110010111000001000
0000000000000000000
00000000000000000000
000000000000000000000
1100101110000010000000
00000000000000000000000
+ 110010111000001000000000
1000000100101110000001010

## Slide 15: Note
We will not be performing difficult addition or multiplication problems in binary
  The computer does these calculations and conversions
  They will be reduced to adding 1 or multiplying by 10

## Slide 16: Verbosity
One weakness of binary numbers is that they are verbose:
  A binary number representing the same quantity as the corresponding decimal number will have approximately 3.322 times as many digits
We will need binary numbers, because that is how almost everything in the computer is stored
  Unfortunately, it’s very difficult to convert from binary to decimal and vice versa… 
999
0b1111100111
10659860817235789230
0b1001001111101111011011101110111101010110011100011100010110101110
2100 – 1 = 1267650600228229401496703205375
0b1111111111111111111111111111111111111111111111111111111111111111111111111111111111111111111111111111
210 = 1024
0b10000000000

## Slide 17: 4-bit translation
Instead, note that there are 16 different quadruple of binary digits:
0b0000 0
0b0001 1
0b0010 2
0b0011 3
0b0100 4
0b0101 5
0b0110 6
0b0111 7
0b1000 8
0b1001 9
0b1010 10
0b1011 11
0b1100 12
0b1101 13
0b1110 14
0b1111 15

## Slide 18: 4-bit translation
Represent every quadruple with a unique digit:
0b0000 0
0b0001 1
0b0010 2
0b0011 3
0b0100 4
0b0101 5
0b0110 6
0b0111 7
0b1000 8
0b1001 9
0b1010 a
0b1011 b
0b1100 c
0b1101 d
0b1110 e
0b1111 f
We ran out of digits…
…we could pick digits
from another language,
say Arabic?
This is called a
look-up table

## Slide 19: 4-bit translation
Always start by grouping binary digits around the radix point and add extra zeros at the start to make a multiple of 4 binary digits:
0b00010010101001001000100110110111
1 2 a 4 8 9 b 7
0b0000 0
0b0001 1
0b0010 2
0b0011 3
0b0100 4
0b0101 5
0b0110 6
0b0111 7
0b1000 8
0b1001 9
0b1010 a
0b1011 b
0b1100 c
0b1101 d
0b1110 e
0b1111 f
This binary number is represented by 0x12a489b7
– We will prefix this with "0x"

## Slide 20: 4-bit translation
To go the other way, just replace of our 4-bit translations by the corresponding quadruple:
6 c f 0 d 5 3 e
0b01101100111100001101010100111110
0b0000 0
0b0001 1
0b0010 2
0b0011 3
0b0100 4
0b0101 5
0b0110 6
0b0111 7
0b1000 8
0b1001 9
0b1010 a
0b1011 b
0b1100 c
0b1101 d
0b1110 e
0b1111 f
This 4-bit translation represents
0b1101100111100001101010100111110
– We stripped off the leading 0

## Slide 21: Hexadecimal numbers
What we are actually doing is representing the numbers in base 16
  This is called hexadecimal (base six-and-ten)
  Often abbreviated as “hex”
  This is where the “x” comes form in "0x"
  Again just like binary uses two digits: 0 and 1
  decimal uses ten digits: 0 through 9
  hexadecimal uses sixteen digits 0 through f
It is used for nothing more than a compact representation of binary
  Conversion between decimal and hex and vice versa is difficult
  To convert between binary and hex is easy
    Just remember to always start at the radix point

## Slide 22: Hexadecimal numbers
What you really need to know for this course: 9 + 1 = a, f + 1 = 10
  These are consecutive hexadecimal numbers
0x27a932f8
0x27a932f9
0x27a932fa
0x27a932fb
0x27a932fc
0x27a932fd
0x27a932fe
0x27a932ff
0x27a93300
0x27a93301
0x27a93302
0x27a93303
0x27a93304
0x27a93305
0x27a93306
0x27a93307
0x27a93307
0x27a93308
0x27a93309
0x27a9330a
0x27a9330b
0x27a9330c
0x27a9330d
0x27a9330e
0x27a9330f
0x27a93310
0x27a93311
0x27a93312
0x27a93313
0x27a93314
0x27a93315
0x27a93316

## Slide 23: Summary
Following this lesson, you now
  Understand that computer use binary numbers
  Know that the digits 0 and 1 are called bits
    Binary numbers are prefixed by "0b"
  See that binary addition and multiplication mirrors decimal addition and multiplication
  Understand that binary numbers are verbose
  and hexadecimal representations are more compact
    Hexadecimal numbers are prefixed by "0x"
  Know how to translate between binary and hexadecimal and back
    You don’t care what decimal value a hexadecimal number is…

## Slide 24: References
[1] Wikipedia:
https://en.wikipedia.org/wiki/Binary_number
https://en.wikipedia.org/wiki/Hexadecimal
https://simple.wikipedia.org/wiki/Hexadecimal_numeral_system

## Slide 25: Colophon
These slides were prepared using the Georgia typeface. Mathematical equations use Times New Roman, and source code is presented using Consolas.
The photographs of lilacs in bloom appearing on the title slide and accenting the top of each other slide were taken at the Royal Botanical Gardens on May 27, 2018 by Douglas Wilhelm Harder. Please see
https://www.rbg.ca/
for more information.

## Slide 26: Disclaimer
These slides are provided for the ece 150 Fundamentals of Programming course taught at the University of Waterloo. The material in it reflects the authors’ best judgment in light of the information available to them at the time of preparation. Any reliance on these course slides by any party for any other purpose are the responsibility of such parties. The authors accept no responsibility for damages, if any, suffered by any party as a result of decisions made or actions based on these course slides for any other purpose than that for which it was intended.