## Slide 1: Binary and hexadecimal numbers

## Slide 2: Outline
In this lesson, we will:
  Review counting
  Consider what happens if we had only eight fingers
  Introduce binary numbers
  Look at addition of binary numbers
  Introduce hexadecimal numbers
  See how hexadecimal numbers an represent binary numbers

## Slide 3: What is main memory?
Main memory is generally volatile memory where any memory location can be accessed as quickly as any other
  Such memory is called random access
Main memory consists of billions of “bits”
  The smallest grouping of bits is a “byte” consisting of 8 bits
    All of main memory is divided into bytes
  A computer with 4 GiB of main memory
  actually has 4 294 967 296 bytes
    This translates into 34 359 738 368 bits

## Slide 4: What is int?
Up to now, we have been using the integer date type int
  Question: how is this stored on the computer?
Answer:
  Every local variable or parameter of type int occupies 32 bits
  The compiler decides where the 32 bits will be in main memory
Recall that when stored in binary,
a number is represented by a sequence of 0s and 1s
  Allocate four bytes for any local variable or parameter declared to be of type int, and then interpret those bits

## Slide 5: How is an integer stored?
With 32 bits,
we could store 32 coefficients of a binary number:
b31b30b29b28b27b26 … b3b2b1b0
The bit labeled bk is the coefficient of 2k
  This is why we always start with the zeroeth bit on the right
  If necessary, bits beyond the most significant 1 are zero

## Slide 6: How is an integer stored?
For example, in this program, the local variable m is stored as
00000000000000000000000000000101
    #include <iostream>
    int main();
    int main() {
    int m{5};
    std::cout << m << std::endl;
    return 0;
    }
  When printed, the 32 bits are interpreted as an integer

## Slide 7: How is an integer stored?
Problem: how do we store negative numbers?
  We need to store either a + or a – a
  To do this, we could allocate one bit to store the sign:
00000000000000000000000000000101
  Our convention could be:
    If the sign bit is 0, the number is positive
    Otherwise, the sign bit is 1, indicating the number is negative
Recall, all these are stored in the computer as voltages in a circuit…
  More in your course on digital circuits and
Proposed location of the sign bit

## Slide 8: Base 2
In a computer,
a number must be stored as a voltage
Having ten different voltages is difficult to design and maintain
  Some of the earliest computers did use base 10
    Back in the 1940s
Instead, it is easiest to have only two voltages:
  0 is represented by 0 V
  1 is represented by 5 V
That is, we only have two digits, 0 and 1
  We will call these bits from binary digits

## Slide 9: Counting
This means we have only two digits now:
0, 1
Thus, the number after “1” is “10”,
so 1 + 1 = 10
also, 10 + 1 = 11
thus, 11 + 1 = 100

## Slide 10: Counting
Therefore, each of these base-2 numbers would represent a certain number of “things”:
0 zero
1 one |
10 two ||
11 three |||
100 four ||||
101 five |||||
110 six ||||||
111 seven |||||||
1000 eight ||||||||
1001 nine |||||||||
1010 ten ||||||||||
1011 eleven |||||||||||
1100 twelve ||||||||||||

## Slide 11: Counting
It is useful to recognize very specific values:
1 one 20
10 two 21
100 four 22
1000 eight 23
10000 sixteen 24
100000 thirty two 25
1000000 sixty four 26
10000000 128 27 100000000 256 28
1000000000 512 29
10000000000 1024 210

## Slide 12: Adding powers of two
Adding numbers in base 10 is something you have learned
  In base 10, adding powers of 10 is easy: 10 + 100 + 10000 = 10110
Adding powers of two (102) in base 2 is also quite easy:
1482
3
0
10
1000
1000000
10000000
100000000
+10000000000
2
8
64
128
256
+1024
1
1
0
1
0
0
1
1
1
0
1

## Slide 13: Representation
In base 10, every digit is associated with a power of 10:
123456789
We will say that:
  The “9” is 9 × 100, so we will say that nine is in the zeroeth position
  The “8” is 8 × 101, so we will say that eight is in the first position
  The “1” is 1 × 108, so we will say that one is in the eighth position

## Slide 14: Representation
To figure out what a binary number represents in decimal, we have
100010011101
  Thus 1 + 4 + 8 + 16 + 128 + 2048 = 2205
20 = 1
22 = 4
23 = 8
24 = 16
27 = 128
211 = 2048

## Slide 15: Adding two binary numbers
1
1
1
1
1
1
1
To add two binary numbers, the process is the same as adding two decimal numbers
  However, you only need to remember that:
    1 + 1 = 10
    1 + 1 + 1 = 11
We can even check our answer:
1 + 4 + 8 + 32 + 64 + 1024 + 2048 = 3181
4 + 32 + 64 + 128 + 1024 = 1252
1 + 16 + 64 + 256 + 4096 = 4433
110001101101
+ 10011100100
1
0
0
0
1
0
1
0
1
0
0
0
1
= 3181 + 1252

## Slide 16: Counting in binary
Question: Is 100 equal to 102 or 4?
  We will usually:
    Prefix binary numbers with "0b"
    Use the monospaced typeface Consolas
  Thus:
    100011010 is a large decimal number
    0b11110110010 is binary for 1970
  To start, we will gray-out the "0b"

## Slide 17: Addition
Just like addition with decimal numbers, you can do the same with binary, you only have to remember:
  1 + 1 = 10 and 1 + 1 + 1 = 11
1 1 1
3725
+ 8982
12707
1 1 1 1 1 1 1 1
9275948135782
+ 503292582385322553
503301858333458335
1 1 1 1
1010
+ 111
10001
1 1 1 1 1 1 1 1 1 1
1110010001100111
+ 110111011011000110
1000101101100101101

## Slide 18: Counting in binary
There are only 10 types of people in the world.
Those who understand binary,
and those who do not.

## Slide 19: Verbosity
It seems it takes more bits to represent a number in binary than it does in decimal
  It’s not that bad:
  it only takes approximately log2(10) ≈ 3.3 times as many bits
  For example, 8357 requires four decimal digits,
  it would require approximately 4 × 3.3 = 13.2
    In fact, it requires fourteen bits: 0b10000010100101
The computer doesn’t care,
but it’s more frustrating for a human to deal in binary

## Slide 20: Base 16: hexadecimal
Suppose instead, we had 16 digits, and not 10:
In base 16,
  a ten
  b eleven
  c twelve
  d thirteen
  e fourteen
  f fifteen
  10 sixteen
0, 1, 2, 3, 4, 5, 6, 7, 8, 9,
a, b, c, d, e, f

## Slide 21: Counting in hexadecimal
Question: Is 5923 equal to 5923 or something else in base 16?
  We will usually:
    Prefix hexadecimal numbers with "0x"
    Use the monospaced typeface Consolas
  Thus:
    5923 is a decimal number
    0x5923 is a hexadecimal number for 22819
  To start, we will gray-out the "0x"

## Slide 22: Verbosity
It seems it takes more fewer hexadecimal digits to represent a number in hexadecimal than it does in decimal
  It’s only slightly better:
  it takes approximately log16(10) ≈ 0.83 times
  as many hexadecimal digits
  For example, 8357 requires four decimal digits,
  it would require approximately 4 × 0.83 = 3.32 hexadecimal digits
    In fact, it still four: 0x20a5

## Slide 23: Why hexadecimal?
Hexadecimal is an easy way to represent a binary number:
0 0b0 0x0
1 0b1 0x1
2 0b10 0x2
3 0b11 0x3
4 0b100 0x4
5 0b101 0x5
6 0b110 0x6
7 0b111 0x7
8 0b1000 0x8
9 0b1001 0x9
10 0b1010 0xa
11 0b1011 0xb
12 0b1100 0xc
13 0b1101 0xd
14 0b1110 0xe
15 0b1111 0xf
0b0000
0b0001
0b0010
0b0011
0b0100
0b0101
0b0110
0b0111
0b1000
0b1001
0b1010
0b1011
0b1100
0b1101
0b1110
0b1111

## Slide 24: Converting binary to hexadecimal
We will only use hexadecimal to easily represent a binary number:
  To convert a binary number to hexadecimal:
    Split the binary number into groups of four
    starting at the least-significant bit
      Pad with zeros to the left if necessary
    Replace each group of four bits with the
    corresponding hexadecimal digit
Thus, in hexadecimal, this binary number is
0x15c68d2ea
0x0 0b0000
0x1 0b0001
0x2 0b0010
0x3 0b0011
0x4 0b0100
0x5 0b0101
0x6 0b0110
0x7 0b0111
0x8 0b1000
0x9 0b1001
0xa 0b1010
0xb 0b1011
0xc 0b1100
0xd 0b1101
0xe 0b1110
0xf 0b1111
101011100011010001101001011101010
000
a
e
2
d
8
6
c
5
1

## Slide 25: Converting hexadecimal to binary
We can easily convert a hexadecimal number back to binary:
  To convert a hexadecimal number to binary:
    Replace each hexadecimal digit with its
    corresponding four bits
Thus, in binary, this hexadecimal number is
0b11111111101000110000011110111000
0x0 0b0000
0x1 0b0001
0x2 0b0010
0x3 0b0011
0x4 0b0100
0x5 0b0101
0x6 0b0110
0x7 0b0111
0x8 0b1000
0x9 0b1001
0xa 0b1010
0xb 0b1011
0xc 0b1100
0xd 0b1101
0xe 0b1110
0xf 0b1111
0xffa307b8
1000
1011
0111
0000
0011
1010
1111
1111

## Slide 26: Counting in hexadecimal
In this course,
you will not be required to add two hexadecimal numbers
You must, however, understand that if you have the hexadecimal number
  0xff3a05
  0x5aff
  0xa5210
  0xff3a04
  0xff3a06
  0x5afe
  0x5b00
  0xa520f
  0xa5211

## Slide 27: Beyond the scope of this course
Now, you could create addition and multiplication tables for both binary and hexadecimal numbers
  You could define binary and hexadecimal multiplication and division
  You could do everything you do with decimal numbers in binary or in hexadecimal
However, you don’t care for this course
  What is covered here is all you will really need:
    Converting between binary and decimal
    Adding two binary numbers
    Converting between binary and hexadecimal
    Understanding the relative order of both binary and hexadecimal numbers

## Slide 28: Summary
Following this lesson, you now
  Understand that computer use binary numbers
  Know that the digits 0 and 1 are called bits
    Binary numbers are prefixed by "0b"
  See that binary addition mirrors decimal addition
  You know that the hexadecimal digits are 0 through 9 and a b c d e f
  Understand that binary numbers are verbose
  and hexadecimal representations are more compact
    Hexadecimal numbers are prefixed by "0x"
  Know how to translate between binary and hexadecimal and back
    You don’t care what decimal value a hexadecimal number is…

## Slide 29: References
[1] Wikipedia:
https://en.wikipedia.org/wiki/Binary_number
https://en.wikipedia.org/wiki/Hexadecimal
https://simple.wikipedia.org/wiki/Hexadecimal_numeral_system

## Slide 30: Colophon
These slides were prepared using the Georgia typeface. Mathematical equations use Times New Roman, and source code is presented using Consolas.
The photographs of lilacs in bloom appearing on the title slide and accenting the top of each other slide were taken at the Royal Botanical Gardens on May 27, 2018 by Douglas Wilhelm Harder. Please see
https://www.rbg.ca/
for more information.

## Slide 31: Disclaimer
These slides are provided for the ece 150 Fundamentals of Programming course taught at the University of Waterloo. The material in it reflects the authors’ best judgment in light of the information available to them at the time of preparation. Any reliance on these course slides by any party for any other purpose are the responsibility of such parties. The authors accept no responsibility for damages, if any, suffered by any party as a result of decisions made or actions based on these course slides for any other purpose than that for which it was intended.