## Slide 1: Floating-point primitive data types

## Slide 2: Outline
In this lesson, we will:
  Review what we have seen about floating-point numbers
  Review scientific notation
  Consider storing approximations of real numbers using fixed precision scientific notation
  Consider some simple examples of arithmetic
  Look at some weaknesses
  Describe ieee754

## Slide 3: Floating-point numbers
Up to this point, we have used the double data type for storing approximation of real numbers
  The name is short for double-precision floating-point data type
There is also a single-precision floating point data type: float
Each only stores approximations of real numbers
  The former with approximately twice as much precision

## Slide 4: Scientific notation
Recall from secondary school scientific notation that allows us to write numbers clearly and succinctly:
Fixed-point notation | Scientific notation
0.0000000000667408 | 6.67408 × 10–11
299792458 | 2.99792458 × 108
0.0000000000000000000000000000000006626070040 | 6.626070040 × 10–34
0.00000000000000000016021766208 | 1.6021766208 × 10–19
8.3144598 | 8.3144598 × 100
3.14159265358979323 | 3.14159265358979323 × 100
6.67408 × 10–11
Significand
Exponent
Base

## Slide 5: Scientific notation
The number of decimal digits used is the precision:
Scientific notation | Precision
6.67408 × 10–11 | 6
2.99792458 × 108 | 9
6.626070040 × 10–34 | 10
1.6021766208 × 10–19 | 11
8.3144598 × 100 | 8
3.14159265358979323 × 100 | 18

## Slide 6: Scientific notation
Without going into detail, each data type has an approximate maximum precision it can store
There is generally only one situation where float has acceptable precision for engineering applications:
  Computer graphics
Data type | Memory used | Approximate maximum precision (decimal digits)
float | 4 bytes (32 bits) | 7
double | 8 bytes (64 bits) | 16

## Slide 7: Scientific notation
This fixed precision leads to some weaknesses
  If the exponent is too large, the number cannot be stored
  There are special values for ±∞ for numbers too large to represent
  There are other values for nan (not-a-number) to represent calculations such as 0.0/0.0 and ∞ – ∞
  Numbers too small are represented by ±0.0
Data type | Minimum | Maximum
float | ± 1.401 × 10–45 | ± 3.403 × 1038
double | ± 4.941 × 10–324 | ± 1.798 × 10308

## Slide 8: Weaknesses
This fixed precision leads to some weaknesses
  It can happen that x + y = x even if y ≠ 0
  The calculation x – y can be problematic if x ≈ y
  Even associativity is lost: sometimes x + (y + z) ≠ (x + y) + z
You will cover these issues in your course on numerical analysis

## Slide 9: Arithmetic
Operations on floating-point data types are more restricted:
  The following binary and unary operators work on double and float:
  + - * / + -
  You can also use the automatic assignment operators associated with the binary arithmetic operators
You cannot use:
  The % operator
  Bitwise or bit-shift operations

## Slide 10: ieee 754-2008
Originally written in 1985, this document specifies the representations of both float and double
Whether you use C++, FORTRAN, Python, or Matlab, your calculations will result in exactly the same result
  Only the quality of your algorithms will affect your outcomes
  Java is not ieee 754 compliant… 
Kahan and Darcy, How Java’s Floating-Point Hurts Everyone Everywhere

## Slide 11: Summary
Following this lesson, you now
  Know floating-point numbers are stored using fixed-precision scientific notation
  Understand that there are issues—they are not perfect
    In a course on numerical analysis, you will learn to mitigate these weaknesses
  The float data type is insufficiently precise for most engineering computation
    Graphics are the one exception…
  Understand that this is defined by the ieee754 standard

## Slide 12: References
[1] Wikipedia:
https://en.wikipedia.org/wiki/Scientific_notation
https://en.wikipedia.org/wiki/Significand
https://en.wikipedia.org/wiki/Double-precision_floating-point_format
https://en.wikipedia.org/wiki/IEEE_754

## Slide 13: Acknowledgements
[1] Zhuo En Dai

## Slide 14: Colophon
These slides were prepared using the Georgia typeface. Mathematical equations use Times New Roman, and source code is presented using Consolas.
The photographs of lilacs in bloom appearing on the title slide and accenting the top of each other slide were taken at the Royal Botanical Gardens on May 27, 2018 by Douglas Wilhelm Harder. Please see
https://www.rbg.ca/
for more information.

## Slide 15: Disclaimer
These slides are provided for the ece 150 Fundamentals of Programming course taught at the University of Waterloo. The material in it reflects the authors’ best judgment in light of the information available to them at the time of preparation. Any reliance on these course slides by any party for any other purpose are the responsibility of such parties. The authors accept no responsibility for damages, if any, suffered by any party as a result of decisions made or actions based on these course slides for any other purpose than that for which it was intended.