## Slide 1: 8 Linear maps and linear operators

## Slide 2: Introduction
In this topic, we will
  Define maps and operators on vector spaces
  Give some background
  Define the image and range of maps
  Give some examples

## Slide 3: Background
In engineering, any signal, be it continuous-time or discrete-time, may be represented as a vector
  Voltages
  Sound
  Temperatures
  Concentrations of chemicals
  Global positioning system coordinates
Engineers must extract information from such signals
output
input

## Slide 4: Background
We may be calculating, for example:
  Average values of a signal or vector
  Reducing noise within a signal
  Increasing the resolution
    Displaying an analog TV signal on a 4K screen
In all cases, the output is another vector
  In the first, the output is R1
  In the second, it is the same vector space
  In the third, it is a higher-dimensional vector space

## Slide 5: Maps between vector spaces
Given two vector spaces U and V , a map A is a function that takes a vector in one vector space and maps it to a vector in another vector space
We will write this as A:U →V
  Here, A must map every vector in U to some vector in V
  We will say u ∈U is mapped to the vector Au ∈V
  We may sometimes write A(u) to avoid confusion,
    For example A(a1u1 + a2u2)
U
V

## Slide 6: Definitions
Given a map A:U →V ,
we will refer toU as the domain
we will refer toV as the codomain
If A:U → U , that is, the domain and codomain are equal,
we will refer to A as an operator
If u ∈U , then Au ∈V is the image of u under the map A
If v ∈V , and u ∈U such that v = Au, we will say u is a pre-image of v under the map A
If S ⊆U , then AS is the collection of all Au where u ∈ S
  AS is the image of S under the map A
Let AU be the collection of all images Au for every u ∈U
  This is said to be the range of A

## Slide 7: Example
Here are examples of two operators, each mapping R3 to R3
  The first maps to cylindrical coordinates
  The second to spherical coordinates

## Slide 8: Example
Here are three other operators
  The first maps the vector to the average value
  The second subtracts off the average of the entries
  The third averages each point with its neighbors

## Slide 9: Summary
Following this topic, you now
  Understand the of a map or operator
    A map takes vectors in the domain and maps them to vectors in the codomain
  Know the terms image and range
    We can take the image of a vector, a subset of the domain, or the entire domain
  Have seen some examples

## Slide 10: References
[1] https://en.wikipedia.org/wiki/Map_(mathematics)
[2] https://en.wikipedia.org/wiki/Domain_of_a_function
[3] https://en.wikipedia.org/wiki/Codomain
[4] https://en.wikipedia.org/wiki/Image_(mathematics)

## Slide 11: Acknowledgments
None so far.

## Slide 12: Colophon
These slides were prepared using the Cambria typeface. Mathematical equations use Times New Roman, and source code is presented using Consolas. Mathematical equations are prepared in MathType by Design Science, Inc.
Examples may be formulated and checked using Maple by Maplesoft, Inc.
The photographs of flowers and a monarch butter appearing on the title slide and accenting the top of each other slide were taken at the Royal Botanical Gardens in October of 2017 by Douglas Wilhelm Harder. Please see
https://www.rbg.ca/
for more information.

## Slide 13: Disclaimer
These slides are provided for the ne 112 Linear algebra for nanotechnology engineering course taught at the University of Waterloo. The material in it reflects the authors’ best judgment in light of the information available to them at the time of preparation. Any reliance on these course slides by any party for any other purpose are the responsibility of such parties. The authors accept no responsibility for damages, if any, suffered by any party as a result of decisions made or actions based on these course slides for any other purpose than that for which it was intended.